## Slide 1: Hydrological Data Screening
Detecting inhomogeneity and trends in
hydrological time series due to climatic and environmental change
Raymond Venneker
UNESCO-IHE Institute for Water Education
Delft, the Netherlands

## Slide 2
Alterations in the hydrological regime occur due to:
  Influence from changing climatic conditions
    GHG emissions, pollution, deforestation, …
  Influence from physical changes at the land surface
    Land use, infrastructure, water use, …
In order to determine the impacts on the hydrology we need data
  Continuous
  Good quality
  Long records
Hydrological Change

## Slide 3
Characteristics of water resources data
Lower bound of zero, negative values often not plausible
Presence of outliers, commonly in high values
Positive skewness, most values in the lower region
Therefore often non-normal distribution
Seasonal patterns are often present
Autocorrelation, mostly positive
Dependence on other variables, e.g. elevation, soils, land use
After: Helsel and Hirsch (2002)

## Slide 4
Time series
A time series represents the values of a variable at successive points in time:
  At point locations, from station observations
  As area-averages, e.g. average rainfall in a river basin
In hydrology and hydrometeorology, time series are discrete, i.e. values at fixed calendar time intervals:
  Fractions of a day, e.g. 30 minutes, 1 hour, 3 hours, …
  Fractions of a year, e.g. 1 day, 1 month, 3 months, …
  Annual series, usually mean value or sum for each year
  5 year moving average/10-year average

## Slide 5
Daily discharge at Lubok Paku, Malaysia, 2001-2006
STL decomposition (Cleveland et al., 1990)

## Slide 6
Components of time series
Periodic variation:
  daily cycles
  Seasonal cycles
Trend:
  Secular trend, systematic increase/decrease over long time periods
  Cyclic trends, irregular variations, e.g. sequences of wet and dry years
Episodic variations due to extreme weather, usually small in number
Random fluctuations, often dominant source of variation in hydrology

## Slide 7
Statistical description
Mean – measure of location
Standard deviation – measure of variation about the mean
Skewness – measure of symmetry about the mean
Standard error (i.e. the standard deviation of the mean):
Coefficient of variation:
See also: DID Manual Vol 4, Ch 5 (2009); Helsel and Hirsch (2002)

## Slide 8
Example: 50 y annual rainfall, Lancang station, China
Mean SD Skew SE CV
1603 187.8 0.4344 26.56 0.1171
Mean + 1 SD
Mean − 1 SD
95% confidence interval of the mean,
Mean ± 1.96 SE
The green line is the apparent trend – needs to be tested if statistically significant

## Slide 9
Min Q1 Median Q3 Max
1183 1490 1600 1723 2085
Tukey’s five-number summary and box plot (Lancang rainfall)
Q3 + 1.5 IQR, or maximum
Q1 − 1.5 IQR, or minimum
First quartile (Q1)
Third quartile (Q3)
Median (Q2)
Inter quartile range:
IQR = Q3 − Q1
Contains 50% of the data
Box plots are useful to visualize and compare distributions. See
Helsel and Hirsch (2002) for further details.

## Slide 10
Autocorrelation
Autocorrelation function (ACF) is the Pearson R for each lag
The lag 1 R is a measure of persistence

## Slide 11
Statistical testing
Statistical tests aim to accept or reject a null-hypothesis, with a specified level of significance, α
A null hypothesis for a specific test can be:
  H0 : There is no trend at significance level α
which leads to the alternative hypothesis:
    H1 : There is a trend at significance level α
A common value for α is 0.01, sometimes 0.1 or 0.05 is also used.
More specific, α is the probability of rejecting H0 while it was actually true. This is called a Type 1 error.

## Slide 12
Test computations (by software)
ts
pdf
−z
+z
0
For a given test, we compute the test statistic from the data, say ts , which follows a certain statistical distribution (e.g. Normal, Student-t)
Then we compute the p value from the probability density function (pdf) of the distribution for test statistic
The null hypothesis H0 is rejected if p ≤ α

## Slide 13
Example: temperature at Lancang station, China

## Slide 14
Step 1: Plot the data and obtain some statistics:
Mean SD Skew SE CV
19.42 0.4322 0.1724 0.06112 0.02225
Min Q1 Median Q3 Max
18.53 19.10 19.40 19.72 20.31

## Slide 15
Step 2: test for absence of persistence (no significant lag 1 autocorrelation)
r(1) = 0.652
Alpha 0.10 0.05 0.02 0.01
UCL 0.233 0.277 0.329 0.364
LCL -0.233 -0.277 -0.329 -0.364
r(1)
UCL (α=0.05)
LCL (α=0.05)
Since r(1) is outside the range [LCL;UCL], we conclude that there is persistence

## Slide 16
Intermezzo: Pre-whitening
The r(1) of the pre-whitened series is inside the range [LCL;UCL]
If significant persistence is present, we have to pre-whiten the data when testing for trend
Pre-whitening removes lag 1 autocorrelation from the series by:
Then, testing persistence for the pre-whitened series:
r(1) = -0.153
Alpha 0.10 0.05 0.02 0.01
UCL 0.233 0.277 0.329 0.364
LCL -0.233 -0.277 -0.329 -0.364

## Slide 17
Since p < 0.05 (< 0.01), H0 is rejected → Temperature increased significantly
Step 3: tests for absence of trend should be non-parametric. That is, no underlying statistical distribution of the data is assumed. There are two tests:
  Test based on Spearman’s rank-correlation coefficient, ρ (rho)
  Test based on Kendall’s correlation coefficient, τ (tau)
The latter, the Mann-Kendall trend test is common in climatology
The test result for our (pre-whitened) temperature data is:
Mann-Kendall trend test (pre-white) :
Series Start = 1960 End = 2009 Length = 50
Null hypothesis: There is no trend in the series
S = 353
tau = 0.2882
p = 0.002875 ***

## Slide 18
Step 4: determine the warming rate
If a significant trend is present, the average rate of increase of decrease can be obtained from the slope of a simple linear regression:
Estimate SE t-stat Pr(>|t|)
Const 18.83 0.06900 272.9 <0.0001 ***
Slope 0.02442 0.002427 10.06 <0.0001 ***
Residual SE: 0.2476 Regression DF: 48
R-squared: 0.6784 Adj R-squared: 0.6717
Temperature rises on average with 0.24 °C in 10 years

## Slide 19
Using DScreen software: Sungai Kerian, Malaysia
Data: annual rainfall (mm) in the Sg. Kerian catchment for 1947-2000
(DID Manual, Vol. 4, 2009)
In Windows explorer, go to the DIDWorkshop folder
Double click on the file DScreen.jar
Select File – Open from the menu bar
Choose the data file TS_Kerian_P_ann.txt

## Slide 20
First year of data
Last year of data
Text output area

## Slide 21
Step 1: plot the time series
Select Plot – Series – Continuous from the menu
(Plot windows stick on the screen until you close them
You can move them to a convenient place
Right-click in plot window opens a menu with options)

## Slide 22
Step 1a: Describe the data
Select Data – Statistics
Select Data – Summary

## Slide 23
Step 2: Check autocorrelation / test persistence
Select Plot – Correlogram
Select Test – Autocorrelation – Persistence (no pre-white)
Verify absence of persistence

## Slide 24
Step 3: Test for trend
Since there is no persistence, pre-whitening is not required
Select Test – Secular trend – Mann-Kendall
There is a
significant
trend if we
can reject the
null hypothesis
Can we?
Note: we can cross-verify using the Spearman test

## Slide 25
Decrease in rainfall of 18 mm per 10 years, too small to be significant
How much is the rainfall amount changing?
Select Data – Apparent trend

## Slide 26
Whole basin at Lubok Paku (25,600 km2):
TS_Pahang_T_ann.txt: annual temperature (°C, 31 y)
TS_Pahang_P_ann.txt: annual rainfall (mm, 31 y)
TS_Pahang_Q_ann.txt: annual discharge (m3/s, 23 y)
Pejabat JPS station (Sg. Kuantan):
TS_Pejabat_P_30mi-max.txt: annual maximum 30 min rainfall (mm, 39 y)
Source: DID data base; Wong et al., Hydrol. Proc. (2010); DID Manual Vol 4 (2009)
Application to Pahang, Malaysia
We carry out a trend analysis for each of the four data sets below
Summarize the outcome